Synchronization and channel coding sublayer
CLTU – Command Link Transmission Unit
Start Sequence / EB90 (hex)	1st / Codeblock	2nd / Codeblock	...	N-th / Codeblock	Tail Sequence / C5 C5 C5 C5 C5 C5 C5 79 (hex) / or 55 55 55 55 55 55 55 55 (hex)
2 byte	8 byte	8 byte		8 byte	8 byte

CLTU total size: variable – 1186 byte max

BCH Codeblock
Information / 56 randomized input data bits	Error Control / 7 Parity bits, 1 Filler bit (=0)
7 byte	1 byte

 Transfer sublayer
TC Transfer Frame
Frame Header	TC Frame Data Unit / = 1 TC Segment	TC Frame Error Control (CRC)
5 byte	variable – 1017 byte max	2 byte

Frame Header
Version (=00)	Bypass Flag	Control Cmd Flag	Spare (=00)	Spacecraft ID	Virtual Channel ID	Frame Length	Frame Sequence Number
2	1	1	2	10	6	10	8
2 byte					2 byte		1 byte

Segmentation sublayer
TC Segment
Segment Header		Segment Data Field
Sequence Flags(=11)	Map ID	Packet #1	...	Packet #n
2	6
1 byte		variable – 1017 byte max

Packet sublayer
TC Space Packet
Packet Primary Header	Packet Data Field
	Packet Secondary Header	User Data Field
	variable	variable
6 octets	1 to 65536 bytes

Packet Primary Header
Packet Version Number / (=000)	Packet ID			Packet Sequence Control		Packet Data Length
	Type (=1)	SHF Flag	APID	Sequence Flags (=11)	Sequence Count
3	1	1	11	2	14	16
	2 byte			2 byte		2 byte