Synchronization and channel coding sublayer
CADU – Channel Access Data Unit
Attached Sync Marker (ASM) / 1ACFFC1D (hex)	Codeblock / (randomized TM Transfer Frame)
4 byte	fixed for mission phase -

 Transfer sublayer
TM Transfer Frame
Transfer Frame Header	Transfer Frame Data Field / = single, several, or partial TM Packet	Transfer Frame Trailer
		Operational Control Field = CLCW	Frame Error Control Field
6 byte	fixed – 2048 byte max	4 byte	2 byte

Transfer Frame Primary Header
Version (=00)	SCID	Virtual Channel ID	OCF Flag (=1)	Master Channel Frame Count	Virtual Channel Frame Count	Frame Data Field Status
					Sec Header Flag (=0)	Sync Flag (=0)	Pkt Order Flag (=0)	Segment Length ID (=11)	First Header Pointer
2	10	3	1	8	8	1	1	1	2	11
2 byte				2 byte		2 byte

Transfer Frame Trailer
CLCW – Command Link Control Word					Frame Error Cntl (CRC)
Ctrl Word Type (=0)	CLCW Version (=00)	Status Fields	COP in Effect (=01)	Virtual Channel ID	Spare	Flags					Farm B Cnt	Spare	Report Value
					No RF Avail	No Bit Lock	Lock-Out	Wait	Re-transmit
1	2	3	2	6	2	1	1	1	1	1	2	1	8
4 byte					2 byte

Packet sublayer

TM Space Packet
Packet Primary Header	Packet Data Field
	Packet Secondary Header	User Data Field
	variable	variable
6 octets	1 to 65536 bytes

Packet Primary Header
Packet Version Number / (=000)	Packet ID			Packet Sequence Control		Packet Data Length
	Type (=1)	SHF Flag	APID	Sequence Flags (=11)	Sequence Count
3	1	1	11	2	14	16
	2 byte			2 byte		2 byte